## Slide 1: GMACS for Scientists
Daniel Fabricant
February 1, 2022

## Slide 2: GMACS Executive Summary
GMACS is GMT’s first-light multi-object optical spectrograph
Wavelength coverage 3300 to 10000 Å in two channels (3300 - 6600 Å) and (6600 to 10000 Å)
Resolution R~1000 to R~6000 with 0.7″ slit width
Field of view is 7´ in the spatial axis, up to 6´ in the dispersion axis
GMACS operates with a wide field corrector/ADC to minimize slit losses due to atmospheric dispersion and to allow long observations of a selected field.
GMACS accommodates 20 on-board laser-cut slit masks for object selection
GMACS will also operate with MANIFEST, GMT’s configurable fiber optic adapter. The initial MANIFEST field of view is 14´ diameter, eventually 20´.

## Slide 3: Contacts
Role | Name | Email (@cfa.harvard.edu)
PI | Daniel Fabricant | dfabricant
Deputy PI | Brian McLeod | bmcleod
Project Scientist/SAC chair | Warren Brown | wbrown
Program Manager | Stuart McMuldroch | smcmuldroch
Project Engineer | Daniel Catropa | dcatropa
Brazilian Lead | Rafael Ribeiro | Steiner Institute

## Slide 4: Frequently Asked Questions
Does GMACS have a flexure control system? Yes, fibers rigidly attached to the slit mask holder are imaged by auxiliary CCDs at the focal plane to detect flexure. The focal plane is mounted on a five-axis stage to remove flexure. Stability goal is <0.25 pixel.
How long does it take to configure for a new field? Less than 300 seconds.
What are the science CCDs? An 8K by 12K array for each channel with 15µm pixels. Deep depletion CCDs will be used in the red.
What is the image scale at the telescope focus? 1″ ≈ 1.04 mm
What is the pixel scale at the detector? A 15µm pixel subtends 0.05″ so binning by ~3 might be typical.
Can GMACS be used as an imager? Yes, but will be limited by scale change with wavelength (lateral color). Do you want to use GMACS as an imager? If so how?
Can GMACS be used with GLAO? Yes
What is the minimum exposure time? ≤ 1 second

## Slide 5: Sample Observing Configurations – 0.7″ Slit Width
Configuration | R | Spectral Range* (Å) | Grating (lpm) | Resolution (Å) | Spectral Range (Å)
Blue, low dispersion | 1020 | 3200 – 6600 (-3´) 3200 – 6600 (center) 3530 – 6600 (+3´) | 500 | 4.95 | 3400
Blue, medium dispersion | 3320 | 4002 – 5227 (-3´) 4400 – 5624 (center) 4783 – 6000 (+3´) | 2000 | 1.52 | 1224
Blue, high dispersion | 5970 | 3200 – 3701 (-3´) 3293 – 3863 (center) 3442 – 4011 (+3´) | 3900 | 0.60 | 570
Red, low dispersion | 1344 | 6600-9525 (-3´) 6600-10000 (center) 6935-10000 (+3´) | 525 | 6.17 | 3400
Red, medium dispersion | 2644 | 6600 – 8751 (-3´) 6904 – 9568 (center) 7700 – 10000 (+3´) | 1000 | 3.14 | 2664
Red, high dispersion | 5895 | 8076 – 9566 (-3´) 8498 – 9988 (center) 8887 – 10000 (+3´) | 1500 | 1.58 | 1480
*Blue bandwidth limited by atmospheric transmission to 3200Å in the blue and by dichroic cutoff near 6600Å in the red. Red bandwidth limited by dichroic cutoff near 6600Å in the blue and CCD response near 10000Å in the red.
Any blue configuration can be used simultaneously with any red configuration
Efficiency will generally fall off for slits placed outside ±2´ due to VPH and binary grating physics